## Slide 1: Host Vulnerabilities
UT CS361S
SpRing 2021
Lecture Notes

## Slide 2: Vulnerabilities and NetSec
This class is “Network Security”
What do host vulnerabilities have to do with it?
Hosts are “nodes” in a network graph
Vulnerabilities can be exploited by remote attackers
  Either to directly access resources on a particular host
  Or, to penetrate network defenses and access a more valuable host

## Slide 3: Brief Overview to Execution
Today: very brief overview of Control Flow Hijacking
  There are other types of vulnerabilities (e.g misconfigured)
  Control Flow Hijacking is probably the hardest to grasp
Critical Concepts:
  The “normal” flow of control for authorized instructions
  Inputs that change the flow to unauthorized instructions
ATTRIBUTION: Derived from slides by Dave Brumley, CMU

## Slide 4: Basic Execution
Process Memory
File system
Binary
Code
Data
...
Stack
Heap
Processor
Fetch, decode, execute
read and write
Notes: What is the name of the register that contains the address of the current instruction?

## Slide 5: Seth’s Notes
Stack
  For temporary static variables
  Function call/return data
  Linear
  Generally, tightly managed
Heap
  Global variables and dynamic variables
  Hierarchical, “free floating”
  Fragmented, not tightly managed

## Slide 6: Seth’s Notes
Assembly “function calls” don’t really exist
  Rather, jump to new location (“function”)
  Save context of old location
  Load context for new location
  Include information for “returning”

## Slide 7: Seth’s Notes
There are multiple ways to do this
“Calling Conventions”
Caller Cleanup – caller cleans stack
Callee Cleanup – called function cleans stack
Other convention variations:
  Order that function data is loaded onto stack
  Whether some data is put into registers instead

## Slide 8: Seth’s Notes
Visualizing caller v callee cleanup
stdcall (callee) cdecl (caller)

## Slide 9: EBP and ESP
EBP
  Stack Base Pointer
  Where the stack was when the routine started
ESP
  Stack Pointer
  Top of the current stack
EBP is a previous function’s saved ESP

## Slide 10: cdecl – default for Linux & gcc
int orange(int a, int b)
{
char buf[16];
int c, d;
if(a > b) c = a;
else c = b;
d = red(c, buf);
return d;
}
…
b
a
return addr
caller’s ebp
callee-save
locals (buf, c, d ≥ 28 bytes if stored on stack)
caller-save
buf
c
return addr
orange’s ebp
…
%ebp
frame
%esp stack
parameter area (caller)
orange’s initial stack frame
to be created before calling red
after red has been called
grow

## Slide 11: GDB Walkthrough
SRC: tenouk.com/Bufferoverflowc/Bufferoverflow3.html
Given C code, examine assembly via GDB
Uses cdecl calling convention

## Slide 12: GDB Walkthrough – C Code

## Slide 13: GDB Walkthrough – Call TestFunc
Register eax loaded with character ‘A’ (0x41), not shown

## Slide 17: GDB Walkthrough – TestFunc() C Code

## Slide 18: GDB Walkthrough – TestFunc() Assembly
32 bytes allocated on stack (0x20). Variables Loaded into this space (not shown).

## Slide 20
Save Registers
Local variables ‘y’ and ‘z’
buff[7] (note, more allocated)

## Slide 21: GDB Walkthrough – TestFunc() Exit

## Slide 23: GDB Walkthrough – TestFunc() Exit, part 2

## Slide 24: GDB Walthrough – Main() after TestFunc() return

## Slide 26: What are Buffer Overflows?
A buffer overflow occurs when data is written outside of the space allocated for the buffer.
C does not check that writes are in-bound
Stack-based
  covered in this class
Heap-based
  more advanced
  very dependent on system and library version
Notes: The key here is predetermined allocation.

## Slide 27: Basic Example
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
27
…
argv
argc
return addr
caller’s ebp
buf (64 bytes)
argv[1]
buf
%ebp
%esp

## Slide 28: “123456”
…
argv
argc
return addr
caller’s ebp
buf (64 bytes)
argv[1]
buf
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
28
return addr
caller’s ebp
123456\0
%ebp
%esp

## Slide 29: “A”x68 . “\xEF\xBE\xAD\xDE”
…
argv
argc
return addr
caller’s ebp
buf (64 bytes)
argv[1]
buf
0xDEADBEEF
AAAA
AAAA… (64 in total)
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
29
%ebp
%esp
corrupted
overwritten
overwritten
Notes: lowest byte of argc is 0; in little endian, that’s the least significant byte

## Slide 30: Frame teardown—1
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
=> 0x080483ff <+27>: leave
0x08048400 <+28>: ret
30
corrupted
overwritten
leave
mov %ebp,%esp
pop %ebp
…
argv
argc
0xDEADBEEF
AAAA
%esp
and
%ebp
%esp
overwritten
Notes: *argc is corrupted because of the null terminator

## Slide 31: Frame teardown—2
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
31
…
argv
argc
0xDEADBEEF
%esp
corrupted
overwritten
leave
mov %ebp,%esp
pop %ebp
%ebp = AAAA
Notes: What to put at 0xDEADBEEF? Or rather, what should we put?

## Slide 32: Frame teardown—3
#include <string.h>
int main(int argc, char **argv) {
char buf[64];
strcpy(buf, argv[1]);
}
Dump of assembler code for function main:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $72,%esp
0x080483ea <+6>: mov 12(%ebp),%eax
0x080483ed <+9>: mov 4(%eax),%eax
0x080483f0 <+12>: mov %eax,4(%esp)
0x080483f4 <+16>: lea -64(%ebp),%eax
0x080483f7 <+19>: mov %eax,(%esp)
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
32
…
argv
argc
%esp
corrupted
%eip = 0xDEADBEEF
(probably crash)
Notes: What to put at 0xDEADBEEF? Or rather, what should we put?

## Slide 33: Shellcode
…
0x080483fa <+22>: call 0x8048300 <strcpy@plt>
0x080483ff <+27>: leave
0x08048400 <+28>: ret
Traditionally, we inject assembly instructions for exec(“/bin/sh”) into buffer.
see “Smashing the stack for fun and profit” for exact string
or search online
…
argv
argc
&buf
…
shellcode…
argv[1]
buf
%ebp
%esp

## Slide 34: Recap
To generate exploit for a basic buffer overflow:
Determine size of stack frame up to head of buffer
Overflow buffer with the right size
computation + control
shellcode | padding | &buf